PALLETIZATION AND WOOD TREATMENT

A.  PALLETS

- A portable platform on which material is placed to facilitate handling and transportation

- Expendable pallets are constructed mostly of fiberboard and intended for discard after one trip

- Permanent pallets are intended for use over several trips

- Most permanent pallets are wood but may also be fabricated from metal or plastic

- Pallet specifications are MIL-P-15011 and NN-P-71

- Pallets allow for either two-way entry or 4-way entry of pallet handling equipment.  Four-way entry is preferred for military shipments

- The standard pallet size is 40” x 48” although other sizes are occasionally permitted

- Pallet Dimensions - when specifying pallet size, the stringer or stringerboard (block pallet) length is always expressed first; for example, a 40" x 48" pallet has a 40" stringer or stringerboard and 48" deckboards.

# B.  PALLETIZED UNIT LOADS—MIL-HDBK-774

- Palletized loads eliminate the handling of individual items or containers, reduce damage, and permit increased storage and stacking heights

- MIL-HDBK-774 is the new designation of MIL-STD-147 for military pallet loads

- MIL-HDBK-774 is to be used for guidance purposes only and may not be cited as a contract requirement

- Standard pallet loads may be up to 43 inches in length, which permits an overhang of 1 ½ inches at each end of the pallet (paragraph 5.1.2)

- Standard pallet loads may be up to 52 inches in width, which permits an overhang of two inches on each end (paragraph 5.1.2)

- Standard pallet load height shall not exceed 54 inches, which includes the height of the pallet (paragraph 5.1.2)

- Maximum gross weight for standard pallet loads is 3000 pounds (paragraph 5.1.1.2)

- See MIL-HDBK-774 for smaller dimensions and weight of MILVAN, SEAVAN, NATO and other specialized load situations

- Loads should be arranged on pallets to eliminate void spaces and provide a level top surface for stacking purposes

- Appendix B provides a useful method to assist with selection of a box loading pattern

- Loads may be bonded to the pallet by using metallic or non-metallic strapping, as well as stretch film or shrink film.  Gluing is permitted only when specified in the contract

- Other storage aids to protect the load are edge protectors, fiberboard wood caps and trays, and wood battens or frames

- Defense Supply Center (DSC) Columbus palletization clause DC1636P001 (latest Revision E) modifies and provides requirements in addition to those of MIL-HDBK-774

- DSC Richmond palletization clause D001450000 (latest Revision C) has specialized requirements for overseas and hazardous shipments as well as for pails and polyurethane containers

- Clauses are available at www.dscc.dla.mil/Offices/Packaging/NMWPMnotice.html

# C.  INSPECTION AND MARKING OF WOOD SHIPMENTS

- Pallets, crates, as well as wood blocking and bracing which meets the heat-treatment standard must show a Heat Treatment (HT) certification stamp

- The stamp can only be applied by contractors who meet the standards of an accredited agency of the American Lumber Standards Committee (ALSC)

- An excellent website with a list of accredited agencies and samples of HT marks is www.dscc.dla.mil/Offices/Packaging/NMWPMnotice.html

- Contractors who make containers or pallets from heat-treated wood must contract with an accredited agency for monthly inspections and process certification in order to be permitted to apply the required HT stamp to their products

- Contractors who buy heat-treated wood products should obtain certification from their vendor that they comply with the ALSC accreditation process

- Current European ruling is that each item must have two HT stamps, though international discussion is ongoing to possibly increase this to four required stamps

- The HT stamp also identifies the accrediting agency trademark, product manufacturer, country code, and the international symbol for no pests.

- The following image is an example of the required HT marking:

- For more information on the wood packing material program refer to the American Lumber Standards Committee web site: http://www.alsc.org/WPM_summary_mod.htm.

# Text boxes

a. Trademark – the identifying symbol, logo or name of the accredited agency

b. Mill Identification – product manufacturer name, brand or assigned mill number

c. Heat Treated Mark

d. Country Code – The two letter ISO country abbreviation

e. Approved International symbol for compliant wood packaging material